## Slide 1: LAB4
VIRTUOSO

## Slide 2: Outline
Virtuoso setup
Create Library
Schematic
Run Spectre simulation

## Slide 3: 1. Virtuoso setup
Step 1: Create and change directory to “layout_env” folder. In this Lab 4, we will work at this place:
%> cd /home/cc??group??/vlsi/${Student_ID}/work/layout_env
Step 2: Copy Sample Environment Kit from Cadence to each of your synthesis working folder
%> cp –rf /home/share_file/cadence/pdk/ pdk

## Slide 4: 1. Virtuoso setup
Step 3: Get license and start virtuoso with a executable file:
Create a file called “go_vir” with the content as follows:
#!/bin/bash –f
cd pdk/gpdk045_v_6_0/
cd /home/share_file/cadence/
source add_path
source add_license
cd –
virtuoso &

## Slide 5: 2. Create Library
Step 1: Open Tools  Library Manager
Step 2: Select File  New  Library and enter a name for the library

## Slide 6: 2. Create Library
Step 3: Tools  Library Manager…
Here you can find all your libraries as well as the built-in libraries and their contents.

## Slide 7: 3. Schematic
Step 1: Create a cell view: Select File  New  Cell View
Name the cell “inv” and click OK.

## Slide 8: 3. Schematic
Step 1: If this pop up appears, choose Always

## Slide 9: 3. Schematic
Step 2: Draw a schematic:
1. select Create  Instance (I) and choose the NMOS transistor

## Slide 10: 3. Schematic
Step 2: Draw a schematic:
2. select Create  Instance (I) and choose the PMOS transistor

## Slide 11: 3. Schematic
Step 2: Draw a schematic:
3. To add pin, Select Create  Pin. (P), then add input, output, vdd and gnd

## Slide 12: 3. Schematic
Step 2: Draw a schematic:
4. Connect the components: Select Create  Wire. (W)
Complete the circuit

## Slide 13: 3. Schematic
Step 2: Draw a schematic:
5. Check and save: Select File  Check and Save.

## Slide 14: 3. Schematic
Step 3: In order to use your cell in a test bench, you first need to create a symbol that represents it.
In order to do that, select Create  Cellview  From Cellview.

## Slide 15: 3. Schematic
Step 4: You can modify the symbol by simply delete things that you don’t want, and add the shape by: (from the Symbol Editor) Create → Shape → Line/Rectangle/Polygon/Circle/…

## Slide 16: 4. Run Spectre simulation
Step 1: To simulate the circuit, we create a new schematic: (from the Library Manager)
File →New → Cellview.
This time, we name it something like sim_inv:

## Slide 17: 4. Run Spectre simulation
To add the cell inv: press I

## Slide 18: 4. Run Spectre simulation
To add VDD and In voltages: press I then browse to vdc in the analogLib library, set DC voltage as 1.8:

## Slide 19: 4. Run Spectre simulation
To add VSS: press I then browse to gnd in the analogLib library:

## Slide 20: 4. Run Spectre simulation
Complete the test circuit.

## Slide 22: 4. Run Spectre simulation
Step 2: Now we will use the tool ADE Explorer to run the analyses.
1. In Schematic Editor, select Launch  ADE Explorer.

## Slide 23
2. From the ADE Explorer,
Setup → Simulator,
then select spectre
4. Run Spectre simulation

## Slide 24: 4. Run Spectre simulation
4. To run a simulation, we need to choose the type of analysis. Select Analyses  Choose…
Select as below
Select Select Component and click on V0 vdc on schematic.
The Start point should be 0, the Stop should be 1.8, the Step Size should be 0.01

## Slide 25: 4. Run Spectre simulation
5. Return back to maestro view
Select Outputs  To Be Plotted  Select on Design.
Point to the In and Out pins on schematic

## Slide 26: 4. Run Spectre simulation
6. To run the simulation, select Simulation  Netlist and Run

## Slide 27: 4. Run Spectre simulation
In case you want to simulate multiple inputs:
Step 1: Change the simulation schematic’s vdc components connecting to the inputs into vpulse
Step 2: Set up the vpulse component
Example: The image is showing a vpulse component moving from 0-1.8V with period 100ns

## Slide 28: 4. Run Spectre simulation
In case you want to simulate multiple inputs:
Step 3: Instead of using the dc analysis mode, use tran for multiple inputs
Example: the image is showing a tran analysis mode running in 500ns

## Slide 29: 5. Submission
This slide just showed an example of an Inverter
Your exercise is to do the same with And gate and Or gate
Each individual submit a report with schematics and simulation of those gates.
There must be your comments showing your own understanding of the schematics and simulation result you submitted in your report